## Slide 1
PVLIB Python 2015
William F. Holmgren1, Robert W. Andrews2, Antonio T. Lorenzo3, Joshua S. Stein4
1Dept. of Atmospheric Sciences, Univ. of Arizona, Tucson, AZ; 2Heliolytics, Toronto, ON;
3College of Optical Sciences, Univ. of Arizona, Tucson, AZ; 4Sandia National Laboratories, Albuquerque, NM
holmgren@email.arizona.edu
https://github.com/pvlib/pvlib-python
42nd IEEE Photovoltaics Specialists Conference
June 14-19, New Orleans, LA
Getting Started with PVLIB
Install the Anaconda Python distribution.
Create a new conda environment:
  conda create –n pvlib
Activate the environment:
  source activate pvlib
Install pvlib
  Latest release: pip install pvlib
  Development: pip install git+https://github.com/pvlib/pvlib-python.git
See documentation and tutorials for help and examples
Why port PVLIB to Python?
The PVLIB Toolbox is a well-established MATLAB library for photovoltaic modeling and analysis. It was originally developed at Sandia National Laboratories and has been expanded by contributions from members of the Photovoltaic Performance and Modeling Collaboration (PVPMC). While MATLAB remains a common choice in many public and private laboratories, the popularity of Python has grown tremendously in the last decade. Python is now the language used in introductory programming courses at a number of top universities. It is elegant, easy to read and write, portable across platforms, free and open source, and it has a large scientific computing community. With the appropriate scientific packages installed (NumPy, SciPy, Matplotlib, statsmodels, pandas), Python provides a powerful alternative to MATLAB and R. The scientific Python stack also enables the use of a single language for the entire data collection, processing, and analysis workflow, which can result in faster development with fewer bugs.
Andrews et. al. introduced the PVLIB-Python toolbox in 2014 and outlined its three main principles:
Take advantage of the Python programming language, to ensure free access to academic and commercial users.
Designed for collaborative development, and backed by a rigorous method to include the contributions of authors and researchers into the package.
Backed by a full testing and validation suite to ensure stability of the package and to allow for validation of model results against real-world performance data.
Overall, the goal of this package is not to supersede other established commercial and public PV modeling packages, such as Helioscope, PVSyst, SAM, and PVWatts.
Instead, PVLIB-Python adds a flexible, accessible, and collaboratively-developed analysis package which can be utilized to derive deep insights about the performance of PV systems and the tools used to model them.
By providing a code-level and modular approach to system modeling, users are able to model and analyze each portion of the PV system performance chain, and are able to utilize the significant data analysis capabilities of Python to analyze large data sets.
The PVLIB-Python source code is hosted on GitHub \cite{pvlib-github}.
The source code to generate the figures in this manuscript and poster is also hosted on GitHub \cite{pvlib-pvsc2015-github}.
Python is elegant, easy to read and write, portable across platforms, free and open source, and it has a large scientific computing community. The scientific Python stack enables the use of a single language for the entire data collection, processing, and analysis workflow, which can result in faster development with fewer bugs. Python provides a powerful alternative to MATLAB and R.
Andrews et. al. introduced the PVLIB-Python toolbox in 2014 and outlined its three main principles:
Take advantage of the Python programming language, to ensure free access to academic and commercial users.
Designed for collaborative development; backed by a rigorous method to include the contributions of authors and researchers.
Backed by a full testing and validation suite to ensure stability of the package and to allow for validation of model results against real-world performance data.
The PVLIB-Python source code is hosted on GitHub.
The PVLIB Toolbox is a well-established MATLAB library for photovoltaic modeling and analysis. It was originally developed at Sandia National Laboratories and has been expanded by contributions from members of the Photovoltaic Performance and Modeling Collaboration (PVPMC).
Introduction to PVLIB
The authors gratefully acknowledge Sandia National Laboratories for the initial development of PVLIB-MATLAB and PVLIB-Python and the ongoing contributions of many others to the project. A list of PVLIB-Python contributors may be found on the GitHub repository and in the online documentation. WFH thanks the Department of Energy (DOE) Office of Energy Efficiency and Renewable Energy (EERE) Postdoctoral Research Award for support. ATL thanks the University of Arizona Renewable Energy Network for support.
Acknowledgements
Fig. 1: Simulation of a fixed-tilt PV system on April 1, 2015, in Tucson, AZ, using PVLIB-Python's implementation of the Sandia Array Performance Model. Currents, voltages, and maximum power are plotted as a function of time of day and effective irradiance. PVLIB-Python was used to load the Sandia Module Database from NREL's website, calculate solar position, clear sky data, airmass, cell temperature, module temperature, and finally run the Sandia Array Performance Model in 9 lines of code. Detailed simulation parameters may be found at this poster’s GitHub repository:
https://github.com/pvlib/pvsc2105
Fig. 3: PVLIB-Python simulation of a single axis tracker, with backtracking, located near Albuquerque, NM, for June 1, 2015. This example simulation used the Ineichen model to generate clear sky DNI, GHI, and DHI, the Hay-Davies model to generate the diffuse plane of array irradiance, and an isotropic ground diffuse model with an albedo of 0.25.
Examples of PVLIB-Python models
Fig. 2: IV curves at different times using the same parameters as Fig. 1. Points represent the 5 points of the SAPM: Isc, Voc, Pmp, Ix, and Ixx.